Quadrature Encoder Interface
STM32F103 Bare-Metal Implementation
Direct Register Access
No CMSIS | No HAL
Using TIM2 Hardware Encoder Mode

---
What is a Quadrature Encoder?
Definition
• A rotary encoder that outputs two signals (A and B) 90° out of phase
• Used for measuring: Position, Speed, Direction
Key Features
• Two output channels: A and B
• 90° phase difference allows direction detection
• Hardware decoding available in STM32 timers
Applications
• Motor position feedback
• Robotic joints
• CNC machines
• Volume knobs

---
Understanding Quadrature Signals
Signal Pattern
Channel A: ___/‾‾‾\___/‾‾‾\___/‾‾‾\___
Channel B: _/‾‾‾\___/‾‾‾\___/‾‾‾\___/‾
Direction Detection
• Clockwise: A leads B (A rises before B)
• Counter-clockwise: B leads A (B rises before A)
Resolution
• 1x mode: Count on A rising edge only
• 2x mode: Count on A rising and falling
• 4x mode: Count on both A and B edges (highest resolution)

---
STM32 Timer Encoder Mode
Hardware Features
• TIM2, TIM3, TIM4 support encoder interface
• Automatic counting (no software intervention)
• Direction handled by hardware
• 16-bit or 32-bit counter (TIM2 is 32-bit)
Encoder Mode Selection (SMCR register)
• Mode 1 (SMS=001): Count on TI1 edges only
• Mode 2 (SMS=010): Count on TI2 edges only
• Mode 3 (SMS=011): Count on both TI1 and TI2 edges
Pin Mapping
• TIM2_CH1 → PA0 (Encoder A)
• TIM2_CH2 → PA1 (Encoder B)

---
Key Registers for Encoder Mode
RCC (Clock Control)
• APB1ENR: Enable TIM2 clock
• APB2ENR: Enable GPIOA clock
GPIO Configuration
• GPIOA_CRL: Configure PA0, PA1 as inputs
Timer Registers
• TIM2_CR1: Control (enable/disable)
• TIM2_SMCR: Slave mode (encoder mode selection)
• TIM2_CCMR1: Capture/compare (input mapping)
• TIM2_CCER: Enable channels
• TIM2_ARR: Auto-reload (counter max)
• TIM2_CNT: Counter value (encoder position!)

---
Step 1: Enable Peripheral Clocks
RCC_APB1ENR Register (0x4002101C)
RCC->APB1ENR |= (1 << 0); // Bit 0 = TIM2EN
• Enables TIM2 peripheral clock
• Without this, timer registers won't respond
RCC_APB2ENR Register (0x40021018)
RCC->APB2ENR |= (1 << 2); // Bit 2 = IOPAEN
• Enables GPIOA clock
• Required for PA0 and PA1 to function

---
Step 2: Configure GPIO Pins
GPIOA_CRL Register (0x40010800)
• PA0 [bits 3:0]: CNF=01 (floating), MODE=00 (input)
• PA1 [bits 7:4]: CNF=01 (floating), MODE=00 (input)
GPIOA->CRL = 0x00000044;
GPIO Mode/CNF Bits
• MODE = 00: Input mode
• CNF = 01: Floating input (default for timer)
• CNF = 10: Input with pull-up/pull-down
Alternative: Input with Pull-up
GPIOA->CRL = 0x00000088; // CNF=10
GPIOA->ODR |= 0x03; // Enable pull-ups

---
Step 3: Set Encoder Mode (SMCR)
TIM2_SMCR Register (0x40000008)
• SMS[2:0] bits select slave mode
Encoder Mode Values
• SMS = 001: Encoder mode 1 (TI1 edges)
• SMS = 010: Encoder mode 2 (TI2 edges)
• SMS = 011: Encoder mode 3 (both edges) ← Best!
TIM2->SMCR = (TIM2->SMCR & ~0x07) | 0x03;
Why Mode 3?
• Counts on all edges → 4x resolution
• Example: 100 PPR encoder → 400 counts/rev

---
Step 4: Map Input Channels (CCMR1)
TIM2_CCMR1 Register (0x40000018)
• CC1S[1:0]: Channel 1 input selection
• CC2S[1:0]: Channel 2 input selection
Configuration
• CC1S = 01: IC1 mapped on TI1 (PA0)
• CC2S = 01: IC2 mapped on TI2 (PA1)
TIM2->CCMR1 = 0x0101;
Optional: Input Filter (IC1F, IC2F)
• Bits [7:4] for IC1, Bits [15:12] for IC2
• Higher value = more filtering (debouncing)
TIM2->CCMR1 = 0x3131; // Filter N=3

---
Step 5: Enable Channels (CCER)
TIM2_CCER Register (0x40000020)
• CC1E: Enable channel 1 capture
• CC2E: Enable channel 2 capture
• CC1P/CC2P: Polarity (0=non-inverted, 1=inverted)
Configuration
TIM2->CCER = 0x0011; // CC1E=1, CC2E=1
Inverting Direction
• If encoder counts wrong direction:
TIM2->CCER = 0x0013; // Invert CC1 polarity
• Or swap A/B wires physically

---
Step 6: Configure Counter Range
TIM2_ARR Register (0x4000002C)
• Sets maximum counter value
• Counter wraps around at ARR value
• TIM2 is 32-bit capable!
TIM2->ARR = 0xFFFFFFFF; // Full 32-bit range
TIM2_PSC Register (0x40000028)
• Prescaler (usually 0 for encoders)
TIM2->PSC = 0; // No prescaling
TIM2_CNT Register (0x40000024)
• This is where you READ the encoder position!
int32_t position = TIM2->CNT;

---
Step 7: Enable the Timer
TIM2_CR1 Register (0x40000000)
• CEN (bit 0): Counter enable
• Other bits usually left at default
Enable Counter
TIM2->CR1 |= 0x01; // Set CEN bit
That's it!
• Timer now counts automatically
• No interrupts needed
• Just read TIM2->CNT when you need position
Reset Counter
TIM2->CNT = 0; // Reset to zero

---
Complete Initialization Code
// 1. Enable clocks
RCC->APB1ENR |= (1 << 0); // TIM2
RCC->APB2ENR |= (1 << 2); // GPIOA
// 2. Configure GPIO (PA0, PA1 floating input)
GPIOA->CRL = 0x00000044;
// 3. Encoder mode 3 (both edges)
TIM2->SMCR = 0x0003;
// 4. Map TI1 and TI2
TIM2->CCMR1 = 0x0101;
// 5. Enable channels
TIM2->CCER = 0x0011;
// 6. Full 32-bit range
TIM2->ARR = 0xFFFFFFFF;
// 7. Enable timer
TIM2->CR1 = 0x0001;

---
Reading the Encoder Position
Get Current Count
int32_t Encoder_GetCount(void) {
return (int32_t)TIM2->CNT;
}
Reset to Zero
void Encoder_Reset(void) {
TIM2->CNT = 0;
}
Calculate Velocity (optional)
// In a timer interrupt (every 10ms):
int32_t delta = TIM2->CNT - last_count;
float rpm = delta * 6000.0 / (PPR * 4);
last_count = TIM2->CNT;

---
Hardware Wiring Diagram
Connections
Encoder STM32F103C8T6
-------- -------------
A ────────► PA0 (TIM2_CH1)
B ────────► PA1 (TIM2_CH2)
GND ────────► GND
VCC ────────► 3.3V or 5V
Notes
• Most encoders have internal pull-ups
• Add 10kΩ external pull-ups if needed
• Check encoder voltage compatibility
• Some encoders have index (Z) output for homing

---
Summary
Key Points
• STM32 has hardware encoder interface
• TIM2/3/4 support encoder mode
• Just 7 register writes to configure
• Counter updates automatically - no CPU load!
Register Sequence
1. RCC→APB1ENR: Enable TIM2 clock
2. RCC→APB2ENR: Enable GPIOA clock
3. GPIOA→CRL: Configure PA0, PA1 as inputs
4. TIM2→SMCR: Set encoder mode 3
5. TIM2→CCMR1: Map inputs
6. TIM2→CCER: Enable channels
7. TIM2→ARR: Set counter range
8. TIM2→CR1: Enable timer
Read Position: TIM2→CNT